## Slide 1
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
1
WiringRobot.ConnectionPointDetector
Finding wire entry points on terminal blocks, straight from the CAD file
Bora Bayrakci
R&D RAS | Friedhelm Loh Group | 14 August 2026

## Slide 2
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
2
What It Does
The problem
• A wiring robot has to know where to push the wire in.
• Today someone teaches every terminal type by hand.
• There are thousands of types in the catalogue. That does not scale.
What my system does
• You give it one CAD file. Nothing else.
• It returns every wire opening: where it is, which way it points, how deep.
• It takes seconds, and it gives the same answer every time.
Why a simple CAD script cannot do this
• A wire opening and a screwdriver opening have the same shape. Only their purpose differs, and shape alone cannot tell you the purpose.
• The manufacturer marks the contact seat, which sits 5 to 25 mm inside the part. The robot needs the mouth on the surface. My system converts one to the other.

## Slide 3
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
3
The Pipeline
STEP file
CAD input
>
Tessellation
gmsh, 0.5 mm
>
Remesh
6 000 vertices
>
Segmentation
4 x DiffusionNet
>
Find openings
connected components
>
Wire / tool filter
random forest
>
Robot output
point + signed axis + depth
Blue boxes are learned. The rest is fixed geometry.
• Remesh: I rebuild every CAD surface at the same point density the network was trained on. Before I did this, the model did not work on real CAD files at all. This one step is what made it work.
• Wire / tool filter: the network can find an opening but cannot say whether a wire or a screwdriver goes in. So I trained a second, small model just for that. It raised precision from 61% to 75%.
• Everything else is deterministic: same file in, same coordinates out.
• Pose and direction correction: once the gate has decided, I move each point sideways onto the opening axis and fix which way the wire goes in. Two small models do that. Without this step I have an opening, not a coordinate.

## Slide 4
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
4
The Models I Used
Component
Method
Function
Training data
Segmentation
DiffusionNet
labels every surface vertex
102 labelled parts
Ensemble
4 models, combined
recovers openings one model misses
4 training runs
Opening extraction
connected components
groups vertices into one opening
none
Insertion axis + pose
ray probing + learned heads
gives the approach vector, then corrects sideways offset and insertion sign
6 330 matched candidates
Wire / tool gate
Random Forest
removes openings that take no wire
1 906 parts
Regime router
Random Forest
selects settings per part
1 906 parts
Two different kinds of training data
• 102 labelled parts are hand-painted vertex by vertex. That is the only way to train this kind of network, and it costs hours per part.
• 1 906 catalogue parts are point lists from the manufacturer. They train the gate and carry every score in this deck.

## Slide 5
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
5
The Words I Use in This Presentation
Term
Definition
Connection point (CP)
one wire opening: position + direction
Mesh / vertex
the 3D surface as triangles; a vertex is a corner
Segmentation
labelling every vertex with what it is
Remeshing
rebuilding the surface at a chosen point density
Ensemble
Signed axis
several models voting together
the direction the wire goes IN, not just the line
Metric
Definition
Precision
of the openings I report, how many are real
Recall
of the real openings, how many I find
F1
precision and recall combined into one score
IoU
how well my labels overlap the correct ones
Dice
same idea as IoU, scored a little more softly
Two words about how I test
• Out-of-fold: a part is only ever scored by a model that never saw it in training.
• Hold-out: a set of parts I locked away before training and opened once, at the end. I did not tune anything against it.

## Slide 6
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
6
Compared to the Master Thesis
Master thesis
My system
Mean IoU (sealed 11-part test)
51.4%
68.0%
Classes over the 50% usable bar
not reported per class
5 of 5
Training data
synthetic plus a little real
1 906 real catalogue parts
Testing
one split
out-of-fold, families kept apart, locked hold-out
What comes out
a labelled surface
point, axis, approach direction, depth
Connection-point F1
not measured, and not measurable from IoU
78.1% detection / 50.4% robot-ready
How I got from the thesis result to mine
• 1. I rebuilt every mesh at one fixed density. The thesis trained and tested on similar meshes; real CAD files look different, and that gap was the whole problem.
• 2. I replaced CAD-derived labels with real catalogue data. CAD labels only agree with a human 46% of the time, so they capped the result.
• 3. I grew the data from 914 to 1 753 parts and added the wire / tool filter, which the thesis does not have at all.
• Why my headline looks lower than 68.0%: the thesis measures one step, I measure four. Surface labelling 68.0% IoU, then find the opening 78.1%, then give an axis 59.0%, then give the axis the right SIGN 50.4%. Each step is a harder question than the one before, and the thesis never asks any of them.
• On the one step we share, I am 16.6 points ahead. The rest is not a worse result, it is a different question.

## Slide 7
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
7
What the Thesis Does Not Solve for a Product
• No coordinates for the robot. The thesis outputs a labelled surface. A robot cannot drive to a colour. I derive the opening mouth, the insertion axis, the approach vector and the depth, so the output is an instruction the robot can execute.
• Wire and tool openings are one class by design. The thesis class Contact covers both the contact and the screwdriver slot. A robot following it would push wire into a tool opening. I added a separate classifier for exactly this decision: precision 60.7% to 75.1%.
• The model does not survive real CAD files. Training and test meshes in the thesis look alike; production STEP files do not. I rebuild every surface at one fixed vertex density before inference, and that is what made the model transfer at all.
• One split can hide a leak. Terminal variants differ by millimetres, so a sibling part on the other side of a random split inflates the score. I group by product family, score out-of-fold, and keep a hold-out that was opened once.
• The product metric is never measured. The thesis reports IoU only, which says how well the surface is labelled, not whether the openings are found. I measure CP-F1 against manufacturer data on 1 906 parts: 76.0%.
• A perfect surface label would still not be enough. I measured where the remaining error sits: it is where the point lands, not which class the vertex got. Ignoring direction entirely buys far less than tightening the position.

## Slide 8
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
8
The Settings I Run With
Geometry parameter
Value
Tessellation deflection
0.5 mm
Vertices per part after remesh
6 000
Spectral basis (k_eig)
96
Minimum opening size
4 vertices
Vertex confidence mask
30%
Terminal merge radius
1.0 mm
Decision parameter
Value
Ensemble members
4
Votes required to keep a candidate
1
Gate rule: score vs the best in the part
50% of the part maximum
Gate rule: absolute floor
20%
Auto-accept gate score
60%
Matching tolerance
6% of part diagonal
• I did not pick these thresholds by eye. I searched them with the part families kept apart, so the search could not cheat. It landed on the value already in the product in 5 out of 5 folds.

## Slide 9
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
9
Segmentation: How Well It Labels the Surface
Mean IoU (metric used by the master thesis)
Score
Difference
Master thesis
51.4%
-
My model, on the sealed 11-part test
68.0%
+16.6 points
Weighted by class size
76.1%
-
Class (sealed 11-part test)
IoU
Above 50%
Housing (the body)
78.9%
yes
Contact (metal contact)
78.7%
yes
LabelSurface (label area)
65.2%
yes
CableEntry (wire opening)
64.8%
yes
SnapPoint (rail clip)
52.3%
yes
What the 50% line means
• 50% IoU is the bar the thesis itself calls usable: above it, the labelled area matches the true area more than it misses it.
• All 5 of my classes clear it. The weakest is SnapPoint, the clip that holds the terminal on the rail, at 52.3%.
• CableEntry, the class the robot actually depends on, sits at 64.8%. Contact, its neighbour, is at 78.7%.
Accuracy 85.8% · Dice 80.5%
• Same classes and same metric as the thesis. This is the sealed 11-part test: three human raters, majority vote, opened once.

## Slide 10
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
10
Connection Points: How Well It Finds the Openings
Evaluation frame
CP-F1
Definition
Detection (does it find the opening)
78.1%
known brand, unseen model [73.8-82.3]
Robot-ready, SIGNED axis (2 mm + 10 deg)
50.4%
what the robot can act on [41.7-58.9]
Robot-ready, axis only (unsigned)
59.0%
the number usually quoted; I quote the signed one [52.4-65.4]
Ceiling: candidate within 10 mm
78.2%
measured: a correctly-aimed candidate is already there
What the wire / tool filter is worth
• Precision went from 60.7% to 75.1% and recall barely moved (68.4% to 65.1%). So three out of four picks are now correct instead of three out of five.
• I report the hold-out number, not the development one. Development numbers in this field run about three times too optimistic, and mine did too.

## Slide 11
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
11
Where It Works Well, and Where It Does Not
Low CP density fewer than 8 connection points
High CP density 8 connection points or more
Share of catalogue
89.5%
10.5%
Representative types
single- and double-level feed-through
distribution and marshalling blocks
CP-F1
78.3%
71.9%
Limiting factor
precision: openings that carry no wire
recall: fewer openings fire at all
Operating mode
automatic
automatic with review
• Low CP density covers 89.5% of the catalogue, so the system is usable across most part numbers today.
• The high-density deficit had an arithmetic cause. 82.7% of those openings occupied fewer than 30 mesh vertices while the extraction filter required 30. Lowering the threshold for this regime moved it from 55.0% to 77.1%.
• Scores are weighted by the true catalogue distribution. An unweighted average over my test sample would have overstated the result by up to 10 points.

## Slide 12
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
12
One Part It Gets Right, One It Gets Wrong
Right: PXC 3213608
• 4 openings out of 4 found, and all 4 pass the robot test. One extra pick. F1 88.9%.
• Position and direction are both inside the robot tolerance on every one of the four.
• Round, recessed openings on one face, well separated.
Wrong: PXC 3071356
• 1 opening out of 4 found, and 5 wrong picks. F1 20%.
• Spring-clamp openings with no round hole. The network does not react to them.
• All six picks came back as review, none as automatic. The system knows it is unsure here.
• Because I know how it fails. Three of the four are simply not seen; the wrong picks are openings that take no wire. Neither is random.
• And I checked that it is not a lack of data. Letting the model train on the exact parts it is tested on only gains 0.3 points.

## Slide 13
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 14.08.2026
13
What I Would Do Next
Next step
Expected effect
Status
Gate acceptance rule: 50% -> 60% of part max
+2.0 points robot-ready, three samples
done
Pose and direction heads (now shipped)
measured end to end, shipped
shipped
Ensembles and augmentation variants
measured; none cleared the noise band
measured, below gate
Higher / lower mesh resolution
re-measured: lower worse, higher inside noise
measured, dropped
Per-vertex offset voting for the opening centre
Data from manufacturers not in training
Three matched runs per segmentation arm
Rebuild the high-CP path end to end
direction learned; magnitude still shrinks
largest single gap; catalogue exhausted
single runs flipped sign four times
four stale steps fixed; selector still from July
trained, needs longer
next
two days
one day
And what I will not claim
The ceiling I can still reach is 78.2%. For that share of the openings a correctly-aimed candidate is already within 10 mm; what is missing is the last few millimetres of position, not the opening itself.
• Threshold tuning is finished, and so is more data from this catalogue. Of 873 parts I was missing, only 7 are published as STEP; the rest exist only in a format a mesh pipeline cannot read. What is left is a new kind of signal.