## Slide 1
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
1
WiringRobot.ConnectionPointDetector
Finding wire entry points on terminal blocks, straight from the CAD file
Bora Bayrakci
R&D RAS | Friedhelm Loh Group | 29 July 2026

## Slide 2
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
2
What It Does
The problem
• A wiring robot has to know where to push the wire in.
• Today someone teaches every terminal type by hand.
• There are thousands of types in the catalogue. That does not scale.
What my system does
• You give it one CAD file. Nothing else.
• It returns every wire opening: where it is, which way it points, how deep.
• It takes seconds, and it gives the same answer every time.
Why a simple CAD script cannot do this
• A wire opening and a screwdriver opening have the same shape. Only their purpose differs, and shape alone cannot tell you the purpose.
• The manufacturer marks the contact seat, which sits 5 to 25 mm inside the part. The robot needs the mouth on the surface. My system converts one to the other.

## Slide 3
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
3
The Pipeline
STEP file
CAD input
>
Tessellation
gmsh, 0.5 mm
>
Remesh
6 000 vertices
>
Segmentation
4 x DiffusionNet
>
Find openings
connected components
>
Wire / tool filter
random forest
>
Robot output
point + axis + depth
Blue boxes are learned. The rest is fixed geometry.
• Remesh: I rebuild every CAD surface at the same point density the network was trained on. Before I did this, the model did not work on real CAD files at all. This one step is what made it work.
• Wire / tool filter: the network can find an opening but cannot say whether a wire or a screwdriver goes in. So I trained a second, small model just for that. It raised precision from 61% to 75%.
• Everything else is deterministic: same file in, same coordinates out.

## Slide 4
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
4
The Models I Used
Component
Method
Function
Training data
Segmentation
DiffusionNet
labels every surface vertex
102 labelled parts
Ensemble
4 models, combined
recovers openings one model misses
4 training runs
Opening extraction
connected components
groups vertices into one opening
none
Insertion axis
ray probing
gives the robot its approach vector
none
Wire / tool gate
Random Forest
removes openings that take no wire
1 906 parts
Regime router
Random Forest
selects settings per part
1 906 parts
Two different kinds of training data
• 102 labelled parts are hand-painted vertex by vertex. That is the only way to train this kind of network, and it costs hours per part.
• 1 906 catalogue parts are point lists from the manufacturer. They train the gate and carry every score in this deck.

## Slide 5
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
5
The Words I Use in This Presentation
Term
Definition
Connection point (CP)
one wire opening: position + direction
Mesh / vertex
the 3D surface as triangles; a vertex is a corner
Segmentation
labelling every vertex with what it is
Remeshing
rebuilding the surface at a chosen point density
Ensemble
several models voting together
Metric
Definition
Precision
of the openings I report, how many are real
Recall
of the real openings, how many I find
F1
precision and recall combined into one score
IoU
how well my labels overlap the correct ones
Dice
same idea as IoU, scored a little more softly
Two words about how I test
• Out-of-fold: a part is only ever scored by a model that never saw it in training.
• Hold-out: a set of parts I locked away before training and opened once, at the end. I did not tune anything against it.

## Slide 6
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
6
Compared to the Master Thesis
Master thesis
My system
Mean IoU (my shipped model)
51.4%
63.3%
Classes over the 50% usable bar
not reported per class
4 of 5 (best model: 5 of 5)
Training data
synthetic plus a little real
1 906 real catalogue parts
Testing
one split
out-of-fold, families kept apart, locked hold-out
What comes out
a labelled surface
point, axis, approach direction, depth
Connection-point F1
not measured
62.5%
How I got from the thesis result to mine
• 1. I rebuilt every mesh at one fixed density. The thesis trained and tested on similar meshes; real CAD files look different, and that gap was the whole problem.
• 2. I replaced CAD-derived labels with real catalogue data. CAD labels only agree with a human 46% of the time, so they capped the result.
• 3. I grew the data from 914 to 1 753 parts and added the wire / tool filter, which the thesis does not have at all.

## Slide 7
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
7
What the Thesis Does Not Solve for a Product
• No coordinates for the robot. The thesis outputs a labelled surface. A robot cannot drive to a colour. I derive the opening mouth, the insertion axis, the approach vector and the depth, so the output is an instruction the robot can execute.
• Wire and tool openings are one class by design. The thesis class Contact covers both the contact and the screwdriver slot. A robot following it would push wire into a tool opening. I added a separate classifier for exactly this decision: precision 60.7% to 75.1%.
• The model does not survive real CAD files. Training and test meshes in the thesis look alike; production STEP files do not. I rebuild every surface at one fixed vertex density before inference, and that is what made the model transfer at all.
• One split can hide a leak. Terminal variants differ by millimetres, so a sibling part on the other side of a random split inflates the score. I group by product family, score out-of-fold, and keep a hold-out that was opened once.
• The product metric is never measured. The thesis reports IoU only, which says how well the surface is labelled, not whether the openings are found. I measure CP-F1 against manufacturer data on 1 906 parts: 76.0%.

## Slide 8
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
8
The Settings I Run With
Geometry parameter
Value
Tessellation deflection
0.5 mm
Vertices per part after remesh
6 000
Spectral basis (k_eig)
96
Minimum opening size
4 vertices
Vertex confidence mask
30%
Terminal merge radius
3.0 mm
Decision parameter
Value
Ensemble members
4
Votes required to keep a candidate
1
Gate threshold, low CP density
40%
Gate threshold, high CP density
35%
Auto-accept gate score
60%
Matching tolerance
6% of part diagonal
• I did not pick these thresholds by eye. I searched them with the part families kept apart, so the search could not cheat. It landed on the value already in the product in 5 out of 5 folds.

## Slide 9
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
9
Segmentation: How Well It Labels the Surface
Mean IoU (metric used by the master thesis)
Score
Difference
Master thesis
51.4%
-
My model, the one in the product
63.3%
+11.9 points
My best model, not shipped yet
68.1%
+16.7 points
Class (product model)
IoU
Above 50%
Housing (the body)
77.3%
yes
CableEntry (wire opening)
68.8%
yes
Contact (metal contact)
64.6%
yes
LabelSurface (label area)
64.2%
yes
SnapPoint (rail clip)
45.4%
no
What the 50% line means
• 50% IoU is the bar the thesis itself calls usable: above it, the labelled area matches the true area more than it misses it.
• 4 of my 5 classes clear it. The one that does not is SnapPoint, the clip that holds the terminal on the rail. It has nothing to do with finding wire openings.
• CableEntry, the class the robot actually depends on, sits at 68.8%.
Accuracy 83.1% · Dice 74.6%
• Same classes and same metric as the thesis. I quote the model I ship, not my best one.

## Slide 10
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
10
Connection Points: How Well It Finds the Openings
Evaluation frame
CP-F1
Definition
The running system
62.5%
what the robot gets today
Robot-ready (2 mm + 10 deg axis)
41.6%
what the robot can actually act on
Same system, weaker split (siblings shared)
77.9%
inflated by geometric twins -- I do not quote it
Ceiling with a perfect filter
89.4%
the best this design could ever reach
What the wire / tool filter is worth
• Precision went from 60.7% to 75.1% and recall barely moved (68.4% to 65.1%). So three out of four picks are now correct instead of three out of five.
• I report the hold-out number, not the development one. Development numbers in this field run about three times too optimistic, and mine did too.

## Slide 11
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
11
Where It Works Well, and Where It Does Not
Low CP density fewer than 8 connection points
High CP density 8 connection points or more
Share of catalogue
89.5%
10.5%
Representative types
single- and double-level feed-through
distribution and marshalling blocks
CP-F1
61.8%
68.2%
Limiting factor
precision: openings that carry no wire
recall: fewer openings fire at all
Operating mode
automatic
automatic with review
• Low CP density covers 89.5% of the catalogue, so the system is usable across most part numbers today.
• The high-density deficit had an arithmetic cause. 82.7% of those openings occupied fewer than 30 mesh vertices while the extraction filter required 30. Lowering the threshold for this regime moved it from 55.0% to 77.1%.
• Scores are weighted by the true catalogue distribution. An unweighted average over my test sample would have overstated the result by up to 10 points.

## Slide 12
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
12
One Part It Gets Right, One It Gets Wrong
Right: PXC 3213608
• 4 openings out of 4 found, nothing invented. F1 100%.
• Direction error 0 degrees, position error 1.3 mm. The robot needs under 2 mm.
• Round, recessed openings on one face, well separated.
Wrong: PXC 3071356
• 0 out of 4 found, and 2 wrong picks. F1 0%.
• Spring-clamp openings with no round hole. The network does not react to them.
• The two wrong picks are screw openings that look the same as wire openings.
I show the failure on purpose
• Because I know why it fails. It is the wire-versus-tool confusion, not random error.
• And I checked that it is not a lack of data. Letting the model train on the exact parts it is tested on only gains 0.3 points.

## Slide 13
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
WiringRobot.ConnectionPointDetector | BORA BAYRAKCI | R&D RAS · 29.07.2026
13
What I Would Do Next
Next step
Expected effect
Status
Retrain the filter on all 1 906 parts
+12.7 points, measured
done
Turn on two modes I already measured
+2.8 points on the older base; needs re-measuring
ready
Try my better segmentation model
4.8 IoU points higher, never tested for F1
untested
Higher mesh resolution for high-CP-density parts
measured: high CP +8.1, low CP -10.8, net -8.8
dropped
A signal that is not geometric
Close the high-CP-density gap
colour was tried and measured flat; still the only way past the ceiling
every error there is a miss, not a wrong pick
open
next
And what I will not claim
• The ceiling is 89.4%. The wrong picks that survive are real openings that simply do not take a wire, and no threshold setting removes them.
• Threshold tuning is finished, and so is more data from this catalogue. Of 873 parts I was missing, only 7 are published as STEP; the rest exist only in a format a mesh pipeline cannot read. What is left is a new kind of signal.