## Slide 1
WiringRobot.ConnectionPointDetector
Automated 3D Connector Component Recognition Pipeline
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
1

## Slide 2
Agenda
1
Problem Statement
2
System Architecture
3
Software Components
4
Machine Learning Backbone
5
Test Results
6
Summary + Latest Developments (Jul)
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
2

## Slide 3
1 Problem Statement
Challenge
Complexity
Manual identification of 3D connector components from CAD data
Error Susceptibility
No automated validation – wiring errors undetected until robot failure
Long Setup Time
Manual geometry configuration required per connector type
No Robot-Ready Output
No structured JSON output for entry point, approach vector, insertion axis
!
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
3

## Slide 4
2 System Architecture
C4 Container Diagram – Pipeline Overview
«person»
User / Operator
[Provides 3D mesh + labels or checkpoint]
Provides mesh + labels or checkpoint
Control Cabinet Component Detection [container]
«component»
meshio
[Loads .off / .obj / .stl mesh files]
«component»
remesh
[Scales to target vertex count (6 000)]
«component»
infer_pipeline
[DiffusionNet / YOLO segmentation]
«component»
connector3d
[3D instance detection & JSON graph]
→ JSON Graph
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
4

## Slide 5
3 Software Components
C4 Component Diagram – Software Funktionsblöcke
«person»
User
[Provides 3D mesh or checkpoint]
Provides mesh + labels or checkpoint
Control Cabinet Component Detection [container]
«component»
meshio
[Extracts mesh data from .off / .obj / .stl]
«component»
remesh
[Generates normalised mesh (6 000 vertices)]
«component»
infer_pipeline
[Pre-processing: DiffusionNet / YOLO segm.]
«component»
connector3d
[Validates 3D instances & builds graph]
Delivers normalised mesh
Passes segmentation label array
Prepares 3D instances
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
5

## Slide 6
3 Software Components
Vision Processing & Detection System
«person»
Operator
[Selects input files + runs CLI]
Uses CLI
Vision Processing System [system]
«container»
infer_ pipeline
[CLI + Orchestration [Python]]
«component»
yolo6.py
[YOLOv6 detection on rendered 6-views]
«component»
diffusionnet.py
[DiffusionNet per-vertex segmentation]
«component»
projection_2d3d.py
[2D detection → 3D crop recovery]
«container»
connector3d
[3D instance graph [Python / NumPy]]
«external»
JSON Graph
[Robot path planning data]
Pose + Graph
«external»
3D Mesh (.off/.obj/.stl)
[Camera / file source]
Image data / file
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
6

## Slide 7
3 Software Components
cp_regressor.py — 7-Channel Per-Vertex Regression Head
«class» CPRegressor
N_CHANNELS : int = 7
backbone : str (mlp | knngraph | diffusionnet)
loss : CPLoss (BCE + MSE + cosine)
+ forward(verts) -> raw (N, 7)
+ pred_to_array(pred, offset_scale) -> array
+ prepare_sample(part, dedup) -> dict
+ train_knngraph_regressor(...) -> (model, meta)
+ train_diffusionnet_regressor(...) -> (model, meta)
Loss:
w_h*BCE(heatmap) + w_off*MSE(offset) + w_dir*(1 - cosine(dir, gt_dir))
Ch
Group
Description / Formula
0
Heatmap
sigmoid(raw) -> [0, 1] -- vertex connection probability
1
Offset dX
( gt_x - v_x ) / mesh_scale [normalised mm]
2
Offset dY
( gt_y - v_y ) / mesh_scale [normalised mm]
3
Offset dZ
( gt_z - v_z ) / mesh_scale [normalised mm]
4
Dir nX
unit vector x -- L2-normalise(pred[4:7])
5
Dir nY
unit vector y
6
Dir nZ
unit vector z
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
7

## Slide 8
3 Software Components
cp_targets.py — Gaussian Encode / NMS Decode Pipeline
ENCODE (ground-truth -> target array)
GT Terminal Block Positions [G x 3]
sigma = heatmap_sigma x bbox_diagonal
h_v = sum_g exp(-||v-g||^2 / 2*sigma^2) [heatmap]
offset = (gt_pos - vertex_pos) / mesh_scale
direction = unit(gt_normal)
-> N x 7 target array
DECODE (predictions -> connection points)
Predicted N x 7 per vertex
Candidate set: vertices where h_v > 0.3
Weighted vote: sum h_v*(v + offset*scale) / sum h_v
NMS radius = max(2*sigma, clearance_mm)
Keep clusters with n_votes >= min_votes
-> Connection Points { point, direction, score }
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
8

## Slide 9
3 Software Components
connector3d.py — Union-Find Clustering & Robot Validation Gate
Union-Find — Fragment Clustering
Fragments
F1
F2
F3
F4
F5
cKDTree.query_pairs(search_r) -> union(i, j)
Instances (connected components)
I1 {F1, F3}
I2 {F2,F4,F5}
I3 {lone}
is_valid_for_robot() — Gate Logic
skew_angle
<= max_skew_deg (75 deg)
x high_skew
feature_area
>= min_area_mm2
x too_small
depth_mm
>= min_insertion_depth_mm
x too_shallow
confidence
>= required_confidence_score
x low_confidence
clearance_mm
>= tool_clearance_mm
x obstruction
ALL checks passed -> is_valid_for_robot = True [OK]
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
9

## Slide 10
3 Software Components
visualization.py — 6-View Orthographic Renderer + Z-Buffer
Six Rendered Views (512 x 512 px each)
+Z TOP
+Y FRONT
-Z BOTTOM
-X LEFT
+X RIGHT
-Y REAR
Axes: +Y = front | +Z = top | +X = right
Per-View Rendering Pipeline
3D Mesh (V, F)
Project vertices -> 2D (orthographic)
Pre-compute per-triangle bounding boxes (numpy)
Rasterize: barycentric interpolation per pixel
Z-buffer test (depth-occlusion culling)
Shade by normal . light_dir
-> 6 x uint8 images (512 x 512 px)
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
10

## Slide 11
3 Software Components
projection_2d3d.py — 2D YOLO Detection -> 3D Mesh Crop Recovery
Render 6 Views
visualization .render_view()
YOLOv6 Detect
yolo6.py predict()
2D Bounding Box
[x1,y1,x2,y2] conf, class
back_project _bb()
2D box -> 3D frustum
vertices_in _frustum()
N_crop verts in region
Mesh Crop
sub-mesh -> connector3d
Key Coordinate Transformations
1. Orthographic Projection
P = M_view * V_world -> (u, v) = (P_x / focal, P_y / focal) + image_center
2. 2D BB -> 3D Frustum
back_project_bb(): (u,v,depth_range) -> axis-aligned 3D bounding volume in world space
3. Frustum Vertex Mask
vertices_in_frustum(): vertex in frustum iff all 6 half-space constraints satisfied
4. Crop Mesh
Face kept iff all 3 corner vertices lie in the masked set -> sub-mesh for connector3d
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
11

## Slide 12
3 Software Components
augment.py — Mesh Augmentation Pipeline for Training Robustness
3D Mesh (V, F, L)
rotate_ mesh()
add_vertex _noise()
smooth_ laplacian()
arap_ deform()
Augmented Mesh
rotate_mesh()
Random rotation around Z-axis theta ~ Uniform[0 deg, 360 deg] v' = R_z(theta) * v Labels: unchanged (rotation-equivariant)
add_vertex_noise()
Gaussian positional noise v' = v + eps, eps ~ N(0, noise_scale) Applied to all vertices independently Labels: unchanged
smooth_laplacian()
Edge-weighted Laplace smoothing 1-3 iterations (config: smooth_iters) v' = sum_j w_ij * v_j / sum_j w_ij Labels: propagated (majority vote)
arap_deform()
As-Rigid-As-Possible deformation Fixed boundary vertices scipy sparse solver (conjugate gradient) Labels: propagated per vertex
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
12

## Slide 13
4 Machine Learning Backbone
Three Backbone Options
MLP
(smoke-test only)
▪ Per-vertex MLP on raw XYZ coords
▪ No geometric receptive field
▪ Memorises geometry — does NOT generalise
▪ Only for overfit / sanity-check runs
▪ No extra dependencies (torch only)
▪ Usage:
▪ python train_cp.py ./data --backbone mlp
KNN Graph (EdgeConv)
(native Windows)
▪ EdgeConv on kNN graph (k=16)
▪ Real geometric receptive field
▪ torch + scipy only — no WSL needed
▪ Runs on native Windows .venv
▪ Best-checkpoint + early-stopping
▪ Usage:
▪ python train_cp.py ./data --backbone knngraph
DiffusionNet
(production)
▪ Spectral diffusion on cotangent Laplacian
▪ Best generalisation on full corpus
▪ Needs robust_laplacian + potpourri3d
▪ Linux / WSL Ubuntu required
▪ Eigenbasis cached per part (op_cache_dir)
▪ Usage:
▪ python train_cp.py ./data --backbone diffusionnet
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
13

## Slide 14
4 Machine Learning Backbone
Training Pipeline & Best-Checkpoint Evaluation
JSON Dataset
json_dataset.py iter_parts()
Sample Prep
cp_regressor.py prepare_sample()
Training Loop
train_knngraph / train_diffusionnet
Val Eval (F1)
_best_ckpt_eval_fn() every N epochs
Best Checkpoint
save_knngraph / save_diffusionnet
Metrics Report
metrics.py aggregate()
early-stop loop (--patience N)
Best-Checkpoint Reload (train_cp.py):
After training, the best-F1 checkpoint is reloaded before final evaluation — ensuring reported metrics reflect the saved model, not the last epoch.
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
14

## Slide 15
5 Connection-Point Graph
Robot-Ready JSON Output Fields
Field
Description
entry_point
World coordinates the robot tool aims for [x, y, z]
approach_vector
Outward direction – where the tool approaches FROM
insertion_axis
Inward travel direction during insertion
insertion_depth_mm
Depth to insert (centroid-based, mm)
insertion_depth_axis_mm
Physical axis-aligned depth span (mm)
confidence_score
Segmentation / detector confidence [0.0 – 1.0]
is_valid_for_robot
Final validity flag after geometry + tool-clearance checks
terminal_type
Terminal hint: screw | spring-cage | push-in | …
Sample Output (one instance)
"entry_point": [120.5, 84.2, 0.0]
"approach_vector": [0.0, 0.0, 1.0]
"insertion_axis": [0.0, 0.0,-1.0]
"insertion_depth_mm": 3.52
"confidence_score": 0.94
"is_valid_for_robot": true
"terminal_type": "screw"
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
15

## Slide 16
5 Test Results
Self-Test Suite – python run_selftests.py
Module
Test Coverage
Status
meshio
load / save OFF, OBJ, STL — round-trip vertex + face assertions
✓ PASS
remesh
simple & loop subdivision — face-count and label-propagation check
✓ PASS
connector3d
build fragments, merge via cKDTree, 3D instance detection
✓ PASS
visualization
render_view vectorised bounding-box — top-view pixel coverage
✓ PASS
json_dataset
stream parts from per-part JSON corpus, validate schema
✓ PASS
cp_targets
encode / decode connection-point targets — sigma + max loc-err
✓ PASS
metrics
precision / recall / F1 + confusion matrix (synthetic CPs)
✓ PASS
cp_regressor
MLP smoke-test — recovers 3 of 3 synthetic connection points
✓ PASS
infer_pipeline
E2E inference pipeline + robustness under 5 / 15 / 30 % label noise
✓ PASS
9 / 9 PASS · 0 FAIL · 0 SKIP — python run_selftests.py
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 11.06.2026
16

## Slide 17
7 Latest Developments
Architecture Pivot — Jun → Jul 2026
Earlier approach (Jun)
▪ Render 6 orthographic views of the mesh
▪ YOLOv6 2D detection → 3D crop recovery
▪ DiffusionNet spectral segmentation
▪ Required WSL / Linux GPU
▪ Learned from rendered 2D images
Current approach (Jul)
▶ STEP B-rep → gmsh tessellation
▶ CAD-direct opening extraction = labels
▶ HierPoint per-vertex 3D regression
▶ Native Windows GPU — no WSL
▶ Learns from 3D geometry directly
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 15.07.2026
17

## Slide 18
7 Latest Developments
Current Pipeline — CAD-Direct + HierPoint
Pipeline stages
▪ STEP file → gmsh tessellation (0.5 mm)
▪ step_openings.py: cylinder/opening → pseudo-labels
▪ HierPoint: FPS pooling + EdgeConv, 7-ch head
▪ Gaussian-vote decode → connection points
▪ Robot-ready JSON (entry_point, approach_vector …)
Scale engineering
▶ Spatial patching of large meshes (full density)
▶ Disk-cached pooling hierarchies (lazy load)
▶ Source-free training — fits a 31 GB box
▶ int32 kNN graphs, chunked forward pass
▶ Single laptop GPU (NVIDIA T1200, 4 GB)
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 15.07.2026
18

## Slide 19
7 Latest Developments
WSCAD Training Corpus
Corpus (v8)
▪ 3033 terminal-block parts (WSCAD-Universe STEP)
▪ CAD-direct labels: 25,529 connection points
▪ Geometry-grouped split — no train/val leakage
▪ 12,556 spatial-patch training graphs
Evaluation protocol
▶ Metric: Jaccard accuracy = TP / (TP+FP+FN)
▶ Frozen val (278) / held-out test (284)
▶ Scored vs CAD labels — no human-GT, no leakage
▶ 5 mm match tolerance, single-shot test
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 15.07.2026
19

## Slide 20
7 Latest Developments
Results — Convergence (Work in Progress)
v31 convergence on WSCAD
▪ F1: ep5 0.706 · ep15 0.771 · ep25 0.804 — climbing
▪ Full-coverage Jaccard 0.55 → 0.67, target ~0.74
▪ Reference: v28 milestone F1 0.898 (earlier corpus)
▪ Training ongoing — not a final number
Post-training levers (no retrain)
▶ Octahedral TTA (axis-preserving) +0.01–0.03
▶ Snapshot ensemble (multi-epoch) +0.01–0.02
▶ Decode calibration (threshold / NMS)
▶ Locked operating point → single-shot test
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 15.07.2026
20

## Slide 21
7 Latest Developments
Selective Prediction — Automation vs Coverage
Concept
▪ Not every part is equally certain
▪ Per-part risk score → abstain on hard parts
▪ Accepted → automated; rest → human review
▪ Report accuracy + coverage + automation yield
Measured (v31, in progress)
▶ ≥ 0.90 Jaccard on least-risky ~40–50 % of parts
▶ Oracle upper bound: 0.90 at ~50 % coverage
▶ Roadmap: better risk score + convergence → 55–65 %
▶ Honest rule: < 50 % ⇒ human-review routing
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 15.07.2026
21

## Slide 22
7 Latest Developments
Key Finding — Ground Truth Sets the Ceiling
What we measured
▪ CAD pseudo-labels vs 9-part human GT: F1 ≈ 0.46
▪ Labels over-mark (mounting/screw/vent holes)
▪ … also under-mark and mis-locate a mid-bore
▪ The model already reproduces CAD labels well
What it means (de-risks the roadmap)
▶ Human-aligned 0.90 needs human labels, not more tuning
▶ Next lever = label quality, not architecture
▶ Plan: 100–150 human-labeled parts as true benchmark
▶ Full-coverage vs selective reported separately
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 15.07.2026
22

## Slide 23
8 Summary
Status & Roadmap
Achieved (Jun → Jul 2026)
▪ CAD-direct labelling: STEP → gmsh → openings
▪ HierPoint backbone on native Windows GPU
▪ WSCAD corpus: 3033 parts, leakage-free split
▪ Honest metric: Jaccard vs CAD labels, no human-GT
▪ Selective prediction + TTA/ensemble harness
▪ 54 automated tests green across the toolchain
Roadmap (next)
▶ Finish v31 convergence + TTA + snapshot ensemble
▶ Improved selective risk score → higher coverage
▶ Human-labeled benchmark → path to aligned 0.90
▶ v32 regularization run (octahedral augment + WD)
▶ Locked single-shot test, then robot integration
ENCLOSURES
POWER DISTRIBUTION
CLIMATE CONTROL
IT INFRASTRUCTURE
SOFTWARE & SERVICE
FRIEDHELM LOH GROUP
R&D RAS | 15.07.2026
23